## Slide 1
CEE 598 — Airport Design
Final Project Report
FAARFIELD-Based CDF Analysis · 6 Airports · 13 Pavement Sections
Chidchanok Pleesudjai
PhD Candidate · School of Sustainable Engineering and the Built Environment · ASU
Spring 2026 · 2026-04-25
VERDICT: 4 OVER · 9 UNDER (PCC fatigue controlling 12 of 13)

## Slide 2
Agenda
▸ Project scope & airports analyzed
▸ What is CDF? — three failure modes
▸ Why AeroPave? Why not just FAARFIELD desktop?
▸ AeroPave architecture — wrapping FAARFIELD 2.1.1's official engine
▸ CDF calculation flow: input → output
▸ The three Nf equations (AC fatigue, PCC fatigue, Subgrade rutting)
▸ Per-section verdicts (4 OVER / 9 UNDER)
▸ Headline finding 1: KMWH C-17 driver
▸ Headline finding 2: KLHX thickness sensitivity case
▸ Field validation — PCI vs CDF (ASTM D5340)
▸ Data quality observations + 130-row gear-coordinate audit
▸ Limitations and conclusions
Chidchanok Pleesudjai · CEE 598 Final Project · ASU Spring 2026
2

## Slide 3
Project Scope
Six airports · 13 pavement sections · all HMA-overlay-on-rigid composites
ICAO | Airport | Sections | Use | Subgrade
KLHX | La Junta Municipal, CO | 2 | Taxiway | Silt Loam (CBR 7)
KPUB | Pueblo Memorial, CO | 1 | Taxiway | Bedrock/Shale (CBR 12)
KMQJ | Indianapolis Regional, IN | 4 | Taxiway | Silty Clay (CBR 4)
KCIU | Chippewa County Intl, MI | 1 | Runway | Fine Sand (CBR 20)
KOTM | Ottumwa Regional, IA | 3 | Taxiway + Runway | Silty Clay Loam (CBR 4)
KMWH | Grant County Intl, WA | 2 | Runway | Gravelly Coarse Sand (CBR 40)
Goal
Use FAARFIELD 2.1.1 to evaluate pavement adequacy (CDF) for 13 sections. Determine whether each section is OVER-designed (CDF < 1.0) or UNDER-designed (CDF ≥ 1.0) for its 20-year design life and projected traffic.
Chidchanok Pleesudjai · CEE 598 Final Project · ASU Spring 2026
3

## Slide 4
What is CDF?
Cumulative Damage Factor · FAA AC 150/5320-6G
Miner's linear damage-accumulation rule: CDF = Σᵢ (nᵢ / N_f,i)
where nᵢ is the number of equivalent design coverages by aircraft i, and N_f,i is the predicted number of coverages to fatigue failure for that aircraft on this pavement structure.
Failure mode | Layer | Eval depth | Response variable
AC fatigue (RDEC) | Asphalt overlay | Bottom of AC | Horizontal tensile strain ε_h
PCC fatigue (2014) | PCC slab | Bottom of PCC | Horizontal flexural stress σ_eff
Subgrade rutting (standard) | Natural subgrade | Top of subgrade | Vertical compressive strain ε_v
Verdict
Section CDF = max(CDF_AC, CDF_PCC, CDF_subgrade) over a 41-point lateral sweep (0–400″ from centerline). CDF < 1.0 → OVER-designed. CDF ≥ 1.0 → UNDER-designed (fatigue failure within design life).
Chidchanok Pleesudjai · CEE 598 Final Project · ASU Spring 2026
4

## Slide 5
Why AeroPave? Why Not Just FAARFIELD Desktop?
Same FAARFIELD engine. AeroPave adds the input-handling and audit layer this 13-section dataset needs.
The dataset that breaks the desktop GUI workflow
6 airports · 13 sections · 859 traffic rows · 229 unique aircraft (ICAO). FAARFIELD desktop's stock library has only 252 aircraft. Of the 229 project ICAOs, roughly 40% (≈90 aircraft) are NOT in FAARFIELD's library and would require manual proxy selection by the engineer in the desktop GUI — for every aircraft, every section.
Library coverage
FAARFIELD desktop
252 aircraft
— would force manual
proxy selection for ~90
project aircraft
— per-engineer judgment
— different engineers,
different answers
AeroPave
1,310 records
— covers ALL 229 ICAOs
in the traffic mix
— enriched library merges
FAA AircraftGeometry.xml
with FAA-ACD
— same source FAARFIELD uses
Audit trail
FAARFIELD desktop
No programmatic way
to prove which aircraft
proxies were used.
— Engineer's notebook
— No verification that
wheel coords reached
the solver unaltered
AeroPave
130-row gear-coordinate
trace audit at 1×10⁻⁶″
— 7 stages per aircraft
— Excel deliverable
(results/gear_coordinate_
trace_audit.xlsx)
— Zero divergences proven
Speed & iteration
FAARFIELD desktop
Manual GUI workflow:
— Re-enter all aircraft
for each section
— No batch mode
— 13 sections × 200+ aircraft
≈ several days of clicks
AeroPave
Programmatic batch:
— 13 sections × full traffic
in 2.5 hours
— Live recompute on input
change (~600 ms)
— Reproducible JSON output
Same engine. AeroPave is the rigorous input + audit layer.
AeroPave does NOT replace FAARFIELD's solver — both tools delegate stress and CDF math to FAARFIELD's compiled DLLs (LEAFClassLib, FaarFieldModel, AMClassLib, FAAMeshClassLib, FEMClassLib).
Chidchanok Pleesudjai · CEE 598 Final Project · ASU Spring 2026
5

## Slide 6
AeroPave Architecture
A wrapper around FAARFIELD 2.1.1's official compiled engine — not a re-implementation
What it is
▸ VB.NET 4.8 / x86 backend wrapping FAARFIELD's compiled DLLs (LEAFClassLib, FaarFieldModel, AMClassLib, FAAMeshClassLib, FEMClassLib, ACClassLib).
▸ React frontend serving as an interactive design-tool + reporting interface.
▸ Stress + CDF math is FAARFIELD's. CDF accumulation is a parity port of modCDF.vb (validated 4580/4580 elements within 0.1% of FAARFIELD desktop printout).
Why use it instead of FAARFIELD desktop directly?
Concern | FAARFIELD Desktop | AeroPave
Aircraft library | 252 stock | 1,310 records (covers all 229 ICAOs)
Aircraft NOT in library | Manual proxy by engineer | Deterministic tiered-match algorithm
Audit trail | Engineer's notebook | results/gear_coordinate_trace_audit.xlsx (130 rows)
Excel-vs-library mismatches | Silently ignored at GUI dropdown | Surfaced with red ≠excel indicator
Verification end-to-end | Trust the GUI | 1×10⁻⁶ inch tolerance trace audit
Chidchanok Pleesudjai · CEE 598 Final Project · ASU Spring 2026
6

## Slide 7
CDF Calculation Flow — Input → Output
Five steps from raw inputs to OVER/UNDER verdict
INPUTS
• Pavement structure • Aircraft library (1,310) • Traffic mix per section
STEP 1 — Resolve geometry
AircraftLibrary. ResolveGeometry(icao, gear, mtow) → wheel_x[], wheel_y[], n_wheels
STEP 2 — Build LEAFACParms
TireX[]=wheel_x, TireY[]=wheel_y TirePress[], NTires, libGear, GearLoad = MTOW × mg_pct
STEP 3 — LEAF stress
clsLEAF.GetResponses (Burmister axisymmetric) → σx, σy, σz, εx, εy, εz
STEP 4 — Three Nf modes
AC fatigue · PCC fatigue (optional FEM aug.) · Subgrade N_f per aircraft × offset
STEP 5 — Aggregate to section CDF
For each lateral offset y_off ∈ {0, 10, …, 400″}:
• Coverages_i = annual_deps × 20yr × growth_factor
• pass-to-coverage from Gauss wander (σ = 30.435″)
• ΔCDF_i = (coverages × p2c) / N_f,i
CDF_section = max over modes, max over offsets
OUTPUT — cdf_results.json
{ icao, section_id, cdf_max, controlling, adequate,
cdf_ac, cdf_pcc, cdf_sub,
cdf_profile_offsets_in[],
cdf_profile_pcc[], cdf_profile_ac[], cdf_profile_sub[],
top_aircraft_full[10] (libGear, wheel_x[], σ_LEAF, σ_FEM…) }
Validated against FAARFIELD desktop
AeroPave's per-element FEM stress was cross-checked against FAARFIELD 2.1.1 desktop's own printout file: 4580/4580 elements within 0.1% of peak (Phase D crosscheck PASS). Same engine, same numbers.
Chidchanok Pleesudjai · CEE 598 Final Project · ASU Spring 2026
7

## Slide 8
The Three Nf Equations
AC fatigue · PCC fatigue · Subgrade rutting — ported from FAARFIELD 2.1.1 modCDF.vb
AC Fatigue — RDEC
ε_h = max(|StrainX|, |StrainY|)
at z = h_AC
PV = 44.422 · ε_h^5.14
· (E_AC × 0.0068948)^2.993
· V_r^1.85 · G_p^(−0.4063)
N_f = 0.4801 · PV^(−0.90074)
where:
V_r = AirVoids/(AirVoids+AsphaltVol)
G_p = (PNMS−PPCS)/P200
E_AC = 200,000 psi (default)
PCC Fatigue — 2014 Model
σ_LEAF = max(|σx|, |σy|)
at z = h_AC + h_PCC
σ_FEM = AMClassLib FEM
σ_eff = max(σ_FEM, 0.95·σ_LEAF)
DF = R / σ_eff
sci_f = 1 − SCI/100
DEN = sci_f·(D−B) + FSlope·B
AA = DF − [sci_f·(A·D−B·C)
+ FSlope·B·C] / DEN
BB = (FSlope·B·D) / DEN
N_f = 10^(AA / BB)
capped at 10^10
Constants A,B,C,D vary with E_sg
Subgrade Rutting — Standard
ε_v = |StrainZ|
at z = Σ h_i (top of subgrade)
A = 0.000247
+ 0.000245·log10(E_sg)
B = 0.0658 · E_sg^0.559
N_f = 10,000 · (A / ε_v)^B
Alt: StraightLine override at
high-departure regime (>10M)
Alt: Bleasdale override (rare)
Source
FullAnalysisWrapper.vb in AeroPave · Verified against FAARFIELD desktop CDF on 13 sections
Chidchanok Pleesudjai · CEE 598 Final Project · ASU Spring 2026
8

## Slide 9
PCC Fatigue — Subgrade-Modulus-Dependent Constants
FAARFIELD's 2014 model: A, B, C, D vary with subgrade modulus E_sg
E_sg range (psi) | Param A | Param B | Param C | Param D
E_sg ≤ 4,500 | 0.76 | 0.16 | 0.857 | 0.16
4,500 < E_sg < 45,000 | 0.76 + (E_sg−4500)·2.54×10⁻⁵ | 0.16 | 0.857 + (E_sg−4500)·2.31×10⁻⁵ | 0.16
E_sg ≥ 45,000 | ≤ 1.027 | 0.16 | 1.794 + (E_sg−45000)·2.54×10⁻⁵ | 0.16
FSlope adjustment
▸ Derived from structural-equivalent thickness of layers above the PCC slab.
▸ Aggregate base factor = 0.5; stiffer materials get up to 1.0.
▸ Polynomial in E_sg/1000 (CompforStab, modCDF.vb:706–755).
▸ Two real bugs caught and fixed during analysis: (1) missing exponent cap of 10 → produced absurd N_f for stiff sections; (2) wrapper had ported the dead legacy 2013 fatigue function instead of the active 2014 model. They diverge by 10–1000× at SR > ~0.4 but agree at the N_f = 10^10 floor.
Validation
Current implementation matches FAARFIELD desktop output on the 13 project sections (this report).
Chidchanok Pleesudjai · CEE 598 Final Project · ASU Spring 2026
9

## Slide 10
Per-Section Verdicts
4 OVER-designed · 9 UNDER-designed · PCC fatigue controlling 12 of 13
ICAO | Section | Use | Layers | CDF (max) | Verdict
KCIU | 21222 | Runway | 2.5" AC + 24" PCC | 76.003 | UNDER
KLHX | 6627 | Taxiway | 2.5" AC + 6" PCC | 6.671 | UNDER
KLHX | 7347 | Taxiway | 2" AC + 10" PCC | 5.04e-03 | OVER
KMQJ | 8640 | Taxiway TWA3 | 3.5" AC + 8" PCC + 6" Stab Base | 18.132 | UNDER
KMQJ | 8662 | Taxiway TWA2 | 3.5" AC + 8" PCC + 6" Stab Base | 18.132 | UNDER
KMQJ | 8780 | Taxiway TWA4 | 3.5" AC + 8" PCC + 6" Stab Base | 18.132 | UNDER
KMQJ | 8881 | Taxiway TWA1 | 3.5" AC + 8" PCC + 6" Stab Subbase | 46.874 | UNDER
KMWH | 37325 | Runway (narrow) | 2" AC + 6" PCC + 12" Agg Base | 2.30e+04 | UNDER
KMWH | 37508 | Runway (wide) | 2" AC + 6" PCC + 12" Agg Base | 2.41e+04 | UNDER
KOTM | 27450 | Runway | 3" AC + 9" PCC | 0.466 | OVER
KOTM | 27641 | Runway | 3" AC + 8" PCC | 0.962 | OVER
KOTM | 28171 | Taxiway | 2.5" AC + 8" PCC | 0.941 | OVER
KPUB | 6948 | Taxiway | 2.5" AC + 7" PCC + 6" P-154 | 9.65e+02 | UNDER
Chidchanok Pleesudjai · CEE 598 Final Project · ASU Spring 2026
10

## Slide 11
Headline 1 — KMWH C-17 Driver
Both runways severely under-designed (CDF ≈ 23,000–24,100). Same root cause: C-17 Globemaster.
Section | Structure | CDF (max) | Verdict | C-17 contribution
KMWH 37325 | 2″ AC + 6″ PCC + 12″ Agg | 2.30×10⁴ | UNDER | C-17 = 14,164 (60%)
KMWH 37508 | 2″ AC + 6″ PCC + 12″ Agg | 2.41×10⁴ | UNDER | C-17 = 14,164 (60%)
Why C-17 dominates
▸ C-17 is a 2T tridem with 12 main-gear wheels (per FAARFIELD's library) — Excel mislabeled it as 2D (8 wheels).
▸ MTOW 585,000 lb · gear load ~556,000 lb spread across 12 wheels.
▸ 895.5 annual departures at BOTH sections (identical) → 17,015 design departures over 20 years.
▸ Identical pavement structure → identical 14,164 contribution to section CDF at both sections.
▸ Marginal CDF spread (~5%) comes from secondary aircraft only (737 MAX 8 +60% at 37508; MRJ-90 only at 37508; C-130J only at 37325).
Field validation
KMWH 37325 shows the highest field load-attributable PCI deduct in the entire study (26.2%). The site that FAARFIELD says is most overloaded by C-17 is also the site where the field shows the most load-related distress. Direct prediction-vs-observation match.
Chidchanok Pleesudjai · CEE 598 Final Project · ASU Spring 2026
11

## Slide 12
Headline 2 — KLHX Thickness Sensitivity
Same airport, same subgrade, same traffic. Only PCC thickness differs. CDF drops 1,300×.
Section | AC | PCC | Subgrade | CDF (max) | Verdict
KLHX 6627 | 2.5″ | 6.0″ | Silt Loam (CBR 7) | 6.67 | UNDER
KLHX 7347 | 2.0″ | 10.0″ | Silt Loam (CBR 7) | 5.04×10⁻³ | OVER
What 4″ of additional PCC buys
▸ C-130 is the controlling aircraft at both — 0.625 annual departures, gear load ~147,000 lb on a Dual Tandem.
▸ At 6627 (6″ PCC): C-130 contributes 5.22 of section CDF 6.67 → ~78% — section fatigues in <4 years.
▸ At 7347 (10″ PCC): C-130 contributes 9×10⁻⁴ of section CDF 5.0×10⁻³ → negligible — 200+ years headroom.
▸ Same engineering load. Same subgrade. PCC thickness is the design lever.
Engineering takeaway
PCC slab thickness is the most efficient single design lever for AC-overlay-on-rigid composites with low-CBR subgrade and moderate aircraft loads. KLHX provides a clean per-airport case study quantifying that lever.
Chidchanok Pleesudjai · CEE 598 Final Project · ASU Spring 2026
12

## Slide 13
Field Validation — PCI vs CDF
ASTM D5340 inspections (58 records, 2005–2023) compared to FAARFIELD prediction
Why raw PCI ≠ CDF
▸ FAARFIELD CDF: predicts STRUCTURAL FATIGUE of the PCC slab (load damage only).
▸ ASTM D5340 PCI: measures VISIBLE SURFACE DISTRESS on the AC overlay (load + climate + age + maintenance).
▸ PCC slab cracks happen UNDER the AC; require years to propagate up and become inspectable. Surface PCI lags structural condition.
The right comparison: load-adjusted deduct
Load-adjusted deduct (LAD) = (100 − PCI_latest) × pct_load_latest / 100
Section(s) | CDF (predicted) | pct_load (field) | Story
KMWH 37325 | 2.30×10⁴ | 26.2% | C-17 traffic showing as load damage — direct validation
KLHX 7347 | 5.04×10⁻³ | 0% | Predicted no load damage; observed none — cleanest negative validation
KMQJ 8881/8662 | 47 / 18 | 11–15% | Mixed deterioration; CDF supported
KOTM 27450/27641 | 0.47 / 0.96 | 0% | Rehab artifact (recent overlay reset PCI to ~95)
KMWH 37508 / KPUB 6948 / KCIU 21222 | 10²–10⁴ | 0% | Climate-only at surface; load damage likely sub-surface
Chidchanok Pleesudjai · CEE 598 Final Project · ASU Spring 2026
13

## Slide 14
Data Quality Observations
Three classes of finding · none affect engineering conclusions · disclosed for reproducibility
1. Excel-vs-library gear-class mismatches (11 aircraft, 38 traffic rows)
▸ Most consequential: C-17 — Excel says 2D (8 wheels); library says 2T (12 wheels).
▸ Both FAARFIELD desktop and AeroPave key on ICAO and read wheel coords from AircraftGeometry.xml. Excel's gear column is documentation only.
2. Layer label inconsistency (KMQJ 8881)
▸ Same physical layer (h=6″, E=500,000 psi, ν=0.20) labeled 'Stabilized Subbase' at 8881 vs 'Stabilized Base' at 8640/8662/8780.
▸ Both labels valid per FAA AC 150/5320-6 for single-stabilized-layer pavements. FAARFIELD's analysis is independent of the label.
3. Per-section traffic allocation
▸ Sections sharing identical structures within an airport record different per-section annual departures for some aircraft.
▸ Legitimate operational reality (different runways/taxiways see different mixes); correctly handled by FAARFIELD.
▸ Dominant aircraft drive the verdict identically across sections; secondary differences produce only marginal spread.
Methodology framing
These observations strengthen the methodology — they document that the analysis pipeline is internally consistent and that input data quirks are handled correctly without modifying the source data.
Chidchanok Pleesudjai · CEE 598 Final Project · ASU Spring 2026
14

## Slide 15
Gear-Coordinate Trace Audit
130 aircraft × section combinations · 1×10⁻⁶ inch tolerance · 7 pipeline stages
What was audited (POST /api/diag/gear-trace)
▸ Stage 1: Traffic input → Stage 2: Library record → Stage 3: ResolveGeometry output
▸ Stage 4: LEAFACParms passed to clsLEAF · Stage 5: LEAFACParms reused by FullAnalysisWrapper for CDF
▸ Stage 6: LEAFACParms before FEM3D PrepareAircraftForFem3d → Stage 7: LEAFACParms after
Audit flag | Count | Meaning
✅ EXACT | 96 | Coordinates pass through every stage unchanged
🟠 SYNTHETIC_DUAL (FEM only) | 34 | Complex gear collapsed to 2-wheel approximation at FEM3D step only · CDF still uses real coords
🔴 DIVERGENCE | 0 | No LEAF/CDF/FEM-pre disagreement detected
⚪ NO_GEOMETRY | 0 | Every consequential aircraft used real-aircraft-derived geometry
Source distribution (130 entries)
▸ xml direct: 79 (61%) · nearest_proxy: 43 (33%) · family_proxy: 5 (4%) · proxy_override: 3 (2%)
▸ 0 gear_template · 0 dual_fallback → no synthetic templates contributed to any verdict
Chidchanok Pleesudjai · CEE 598 Final Project · ASU Spring 2026
15

## Slide 16
Limitations and Future Work
▸ PCI inspections lag structural condition. Sections predicted under-designed but currently showing 0% load-attributable deduct (KMWH 37508, KPUB 6948, KCIU 21222) most likely have sub-surface PCC slab fatigue not yet visible at the AC surface. Falsifying would require FWD/GPR or longer observation windows.
▸ 13-section CDF cross-check against FAARFIELD desktop GUI is recommended as additional validation. Phase D crosscheck (FEM stress) PASSED; full CDF cross-check is outside this project's scope.
▸ 3D FEM mesh visualization collapses complex-gear aircraft (C-17, B788, B789, K35R) to a synthetic 2-wheel dual approximation — a documented FAARFIELD managed-FEM limitation. CDF uses real wheel layout (verified by audit); only 3D visualization shows the approximation. Does NOT affect the verdict.
▸ PCC modulus of rupture R is set to 700 psi (FAARFIELD default) for most sections. Older sections (PCC age > 20 years) could justify R reduction to ~360 psi (FAA AC 150/5320-6F lower bound). Current results are slightly optimistic for those sections.
▸ Subgrade modulus is derived from NRCS Web Soil Survey CBR via E_sg = 1500·CBR. Site-specific FWD-derived moduli would tighten the prediction.
Chidchanok Pleesudjai · CEE 598 Final Project · ASU Spring 2026
16

## Slide 17
Conclusions
4 OVER · 9 UNDER · PCC fatigue dominant · methodology validated by 130-row audit
▸ Of 13 sections analyzed across 6 airports, 9 are predicted under-designed (CDF ≥ 1) and 4 over-designed (CDF < 1).
▸ PCC fatigue is the controlling failure mode for 12 of 13 sections; subgrade rutting controls one.
▸ Most severe under-design at KMWH (CDF ≈ 23,000–24,100) is driven by C-17 Globemaster on a 6″-PCC slab. Field PCI at 37325 shows the highest load-attributable deduct in the entire study (26.2%) — direct field validation.
▸ Cleanest design-margin demonstration is at KLHX: 4″ of additional PCC reduces CDF by ~1,300× for the same traffic.
▸ Field validation across the 13 sections supports FAARFIELD predictions where surface distress has had time to manifest. Most sections show climate-dominated surface aging (not predicted by load-only CDF) — expected for AC-overlay-on-rigid composites at mid-life.
▸ 130-row gear-coordinate trace audit at 1×10⁻⁶ inch tolerance: zero divergences. Wheel coordinates from the enriched library reach the LEAF and CDF solvers unaltered for every aircraft × section combination.
Chidchanok Pleesudjai · CEE 598 Final Project · ASU Spring 2026
17

## Slide 18
Thank you
Questions?
Chidchanok Pleesudjai · cpleesud@asu.edu
Companion report: results/CEE598_Final_Report_PleesudjaiC.docx
Audit Excel: results/gear_coordinate_trace_audit.xlsx (130 rows, 0 divergences)